## Slide 1
DEVELOPMENT OF APTAMER BASED LATERAL FLOW IMMUNOCHROMATOGRAPHY STRIP TEST FOR HALAL AUTHENTICATION OF PHARMACEUTICAL PRODUCTS CONTAIN GELATIN
Hari Widada1,2, Abdul Rohman2, Ririrs Istifgfarie Jenie2, Sismindari2
School of Pharmacy, Faculty of Medical and Health Sciences Universitas Muhammadiyah Yogyakarta, Yogyakarta, Indonesia1
Doctoral Programme, Faculty of Pharmacy, Universitas Gadjah Mada, Yogyakarta, Indonesia2
sismindari@ugm.ac.id
ABSTRACT
The development of non-halal component detection technology is important because there are many cases of mixing non-halal ingredients with halal ingredients. The halal contaminant detection tool that can be applied in the field quickly, efficiently, portable and can be used for large amounts of samples such as the current strip test is still limited and must be imported from abroad. This study aims to develop rapid detection of halal contaminants in food and pharmaceutical products with apatamer-based lateral flow immunochromatography (single-strand oligonucleotides / ssDNA). The principle of making immunochromatographic test strips is to conjugate colloidal gold as a marker with aptamer. This conjugate is placed on the conjugate pad, one part of the immunochromatographic strip test system. Analysis of food/ pharmaceutical products with immunochromatographic test strips using samples made with gelatin, both references from bovine, porcine, vegetable gelatin and a mixture of gelatin from bovine-porcine and vegetable-porcine and also pharmaceutical products in the form of capsules on the market. The results of this research up to this stage have been obtained by the oligonucleotide sequence (ssDNA aptamer) which will be used to design the LFI test strip. One of the sequences is as follows: 5 '-GCCTAAAATCTCCCCTCCATGGATA- TGCCTAAATCTTCC-CTCAATGGTATGGCTAAATCTCCCCCCCCCGTAAGGCTAAA-TCTTCCTT-3'. Furthermore, aptamer candidates who will be used as biosensors will be purchased from suppliers in the modified position 5 'so that it can be applied in the LFI strip test system.
Keywords: Lateral Flow Strip Test, Aptamer, porcine gelatin
Materials
HAuCl4·3H2O, Tris (2-carboxyethyl) phosphine (TCEP), bovine serum albumin (BSA), ovalbumin (OVA), DTT and streptavidin were provided by Sigma-Aldrich (St. Louis, MO, USA). Sodium hydrogen phosphate (Na2HPO4), monobasic potassium (KH2PO4), sodium chloride (NaCl), potassium chloride (KCl) and other reagents were from Beijing Chemical works (Beijing, China). Ethyl acetate (HPLC grade) was purchased from Fisher Scientific (Fisher Scientific, Fair Lawn, NJ, USA). Water was obtained from a Milli Q purification system (Millipore). All other inorganic chemicals and organic solvents were of analytical grade or better. purchased from Sigma Aldrich. Aptamer 5’-GCCTAAATCTCCCCTCAAT
GGTATGCCTAAATCTTCCCTCAATGGTATGG CTAAATCTCCCCCCGAAAATCTAT
TTGCCTCTTTCATTTTTTTTTTTTTTTTTTTTT-SH-3’, probe-1 5’-ATGAAAGAGGC AAATAGATTTTCGGGGGGAGATTTAGCCATACCATT GAGGGAAGATTTAGG
CATATTGATATTGAGGGGAGATTTAGGC-Biotin-3’ and probe-2 5’-ATGAAAGAGGC AAATAG ATTTTCG GGGGGAGATTTAGCCATACC ATTGAGGGAAGATTTAGG CATATTGATATT GAGGGGAGATTTAGGC-Biotin-3’ were purchased form IDT (USA).
Introduction
A good technique must be supported by adequate laboratory equipment, so that it can detect counterfeiting and differentiate mixtures which are critical points in the authentication of halal products. Molecular biology-based methods, such as polymerase chain reaction (PCR), Real-Time PCR (Rodriguez et al., 2005), Restriction Fragment Length Polymorphism (RFLP) analysis (Chen et al., 2010), multiplex PCR (Ghovvati et al. , 2009), and species-specific PCR (Man et al., 2007). Another method developed for the detection of components from pigs in food is a DNA-based method by exploring aptamer specific to selected porcine gelatin using the SELEX (Systematic Evolution of Ligands by Exponential Enrichment) method. This research will develop rapid detection devices in the form of strip tests with the target of porcine gelatin in pharmaceutical products with aptamer as biosensor.
Reference
Chen, S.-Y., Liu, Y.-P., Yao, Y.-G., 2010, Species authentication of commercial beef jerky based on PCR–RFLP analysis of the mitochondrial 12S rRNA gene. Journal of Genetics and Genomics 37 (11), 763–769
Ghovvati, S., Nassiri, M.R., Mirhoseini, S., Moussavi, A.H., Javadmanesh, A., 2009, Fraud identification in industrial meat products by multiplex PCR assay. Food Control 20 (8), 696–699
Man, Y.B.C., Aida, A.A., Raha, A.R., Son, R., 2007. Identification of pork derivatives in food products by species–specific polymerase chain reaction (PCR) for halal. Food Control 18 (7), 885–889
CP: Hari Widada
School of Pharmacy, Universitas Muhammadiyah Yogyakarta, Yogyakarta, Indonesia.
Email: hr.widada@gmail.com
Methods
1. Preparation of Gold Nanoparticles
AuNPs diameter’s is 10 nm
HAuCl4.3H2O 1% + Na-Sitrat 1%
Preparation of Aptamer-AuNPs Conjugate
Conjugation AuNPs with SH-Aptamer
Optimization by adding DTT
Preparation od Test Line & Control Line
Using streptavidin-biotin raction
Consist of DNA probe1&2
Figure 1. SELEX procedure
modifierd by adding
graphene oxide (GO)
Design of Lateral Flow Strip Test
Results and Discussion
Figure 2. Sequencing results of aptamer candidate for biosensor
No | Name | Spesification
1 | Conjugate SH-Aptamer | 5’- GCC TAA ATC TCC CCT CAA TGG TAT GCC TAA ATC TTC CCT CAA GG TAT GGC TAA ATC TCC CCC CGA AAA TCT ATT TGC CTC TTT CAT TTT TTT TTT TTT TTT TTT TT-SH-3’
2 | Probe-1 | 5’-ATG AAA GAG GCA AAT AGA TTT TCG GGG GGA GAT TTA GCC ATA CCA TTG AGG GAA GAT TTA GGC ATA TTG ATA TTG AGG GGA GAT TTA GGC-Biotin-3’
3 | Probe-2 | 5’-AAA AAA AAA AAA AAA AAA AA-Biotin-3’
Conclusion
Aptamer can be selected by the GO-SELEX method by using a target of pig gelatin. Selected aptamers have the potential to be designed as biosensors for lateral flow strip test models.
Acknowledgements This Projects supported by Ministry of Research, Technology and Higher Education of the Republic of Indonesia contributed to this study.